## Slide 1: MALAVIYA NATIONAL INSTITUTE OF TECHNOLOGY CENTRE FOR ENERGY AND ENVIRONMENT
LOAD AND DEMAND FORECASTING
Prepared by
Bala Ganesh K
2020PCV5316
Submitted to
Dr. Parul Mathuria
Assistant Professor

## Slide 2: Table of Contents
Electric Load Forecasting
Load Forecasting Categories and Classifications
Duration based Forecasting
Simple and Advanced Techniques
End Use Method
Econometric Approach
Input Output Model
Scenario based Approach
ANN based Approach
Hybrid Approach
Energy Demand Analysis

## Slide 3: Electric Load Forecasting [5]
Electricity is a clean, efficient source of energy suitable for environment-friendly society
Has different characteristics compared to material products like cannot be stored in bulk
Accuracy of forecasting is important to save O&M costs and make correct decisions for future development of grid
Electricity Load Forecasting
Capacity Scheduling
Power Systems Management
Economic development
National Security
Daily Operation of society
Smart Grid, EVs and RES integration with increasing population and living standards improvement
Demand pattern is complex due to the deregulation of markets
Factors affecting Accuracy
Weather
Time
Economy
Random disturbances
Consumer practices
Climate Change

## Slide 4: Load Forecasting Categories and Classifications [5]
Long Term Forecast
1 to 20 years
Strategic planning & establishment of new power infrastructure
Medium Term Forecast
1 week to 1 year
Maintenance scheduling, fuel purchases, energy trading
Very Short Term Forecast
1 hour to 1 week
Day to day utility operations, generation and transmission scheduling
Short Term Forecast
Regression Analysis, Scenario based
Regression Analysis, Machine Learning
Machine Learning, AI models
Real time control
AI models
Forecasting models
Multi-factor
Time-Series
Multi-factor methods
Causal relationships between influencing factors and forecasting values
Time Series methods
Avoids the complicated and non-objective factors
Relies on historical data
Easier and quicker
Statistical models
Machine Learning models
Hybrid models

## Slide 5: Duration based Forecasting [2], [3]
End Use method
Econometric method
Combines economic theory and statistical techniques
Uses of electricity in the residential, commercial, and industrial sector
Demand derived from customer's demand for light, cooling, heating, refrigeration, etc.
Demand as a function of the number of appliances in the market
Estimates relationships between energy consumption (dependent variables) and factors influencing consumption (independent variables)
Medium and Long Term Forecasting Methods
Short Term Forecasting Methods
Similar day approach
Regression models
Time Series models
Neural Networks
Expert Systems
Fuzzy Logic Systems
Statistical Learning algorithms

## Slide 6
End Use Method [3], [4]
Bottom up approach & mostly under forecast
Requires analysis of utility function of consumers belonging to every segment
Focus on final needs at a disaggregated level
Aggregates demand by consumer categories
Demand calculated based on the use of various electric appliances
Incorporates energy efficiency improvements & changes in energy-mix
Future values of saturation are forecasted exogenously using economic & demographic variables
Future appliance saturation is theorized to grow along an S-shaped curve
Past surveys identify current position on curve and future saturations are extrapolated from there
Suitable for both energy and power demand forecast
Econometric Approach [3], [4]
Econometrics is the integration of economics, mathematics and statistics
Obtains values of parameters that are coefficients of mathematical form of economic relationships
Statistical methods which help in explaining the economic phenomenon are adapted as econometric methods
Used to find stochastic relationship in mathematical format
Relevant variables are used in model and rest are dumped as disturbances or random variables
Mathematical model is exact while statistical model contains a stochastic term
Model consists of (i) set of equations containing observed variables (ii) statement about errors in observed values of variables (iii) specification of probability distribution of disturbances.
Data types used in estimation: Time series, Cross section, Panel & dummy variable

## Slide 7
Major Types of Basic Forecasting Methods [5]
Forecasting methods
Quantitative/
Objective
Regression Analysis
Decomposition methods
Qualitative/
Subjective
Subjective Curve Fitting
Technological Comparisons
Delphi Method
Box-Jenkins Methodology
Exponential Smoothing
Regression Approach [7]
Regression is a very widely used statistical technique
Model considers relationship of load consumption and other factors that affect it such as weather conditions, economic and time factors
Mathematical model is written as
L(t) = Ln(t) +

## Slide 8: Input Output Model [6]
Statement of problem under consideration
Choice of relevant variables
Collection of data on relevant variables
Specification of model
Choice of method for fitting the data
Fitting of model
Model validation and criticism
Model for solution of the proposed problem.
Steps in Regression Analysis [4]
Provide a framework that is able to capture the direct as well as indirect energy demands through inter-industry transactions
Highly data-intensive approach
Short-Term Load & Price Forecasting System
Short-Term Forecasted load
Short-Term Forecasted price
Historical load data
Historical price data
Climatic data
Smart technologies penetration
Ratio of different customer types

## Slide 9
FORECASTING MODELS [5] |  |  | 
Statistical Models | Artificial Intelligence/Machine Learning Models |  | Hybrid Methods
Moving Average | Extreme Learning Machines |  | 
Box-Jenkins | Support Vector Method |  | 
ARIMA | Fuzzy Logic |  | 
ARMAX & ARIMAX | Wavelet Network |  | 
Kalman Filter | Genetic Algorithm |  | 
Grey | Expert System Based |  | 
Exponential Smoothing |  |  | 
Auto Regressive | Artificial Neural Networks | Back Propagation | 
 |  | Radial Basis Function | 
 |  | Random | 
 |  | Self-Organizing | 
 |  | Feed Forward | 
 |  | Recurrent | 
Basic Classification of Forecasting Models [5]

## Slide 10: Simple and Advanced Techniques [1], [5], [7]
Modern/Advanced
Artificial Neural Networks (ANN)
Expert Based Systems
Traditional/Simple
Regression approach
Multiple regression
Exponential smoothing
Iterative reweighted least-squares
Stochastic time series
Support vector machine
Genetic Algorithm
Particle Swarm Optimization (PSO) Algorithm
Fuzzy Logic system
Multiple Regression
Factors like weather, economic growth, electricity prices etc.
Principle of least-square estimation
Mathematical model given as
Yt = vtat + t
t  sampling time
Yt  measured system total load
vt  vector of adapted variables (time, temp., light intensity, wind speed, humidity etc.)
at  transposed vector of regression coefficients
t  model error at time t.
Exponential Smoothing (ES)
Exponentially weighted average data of past observations to predict the future load
Exponential decay of influence of past historical data by appropriate weightage allotment
Good accuracy, simplicity, robustness, and low cost
Accuracy of model depends on smoothing coefficients
Single (SES) (Brown’s method)
Requires little calculation
Data pattern neither has cyclical or seasonal variation, nor trend in historical data
Double (DES) (Holt’s method)
Used in economics
Enable the forecasted values with a trend included
Triple (TES) (Holt-Winters method)
Additive
If original data shows stable seasonal functions
Simple
Multiplicative
If original data reflects variations of seasonal fluctuations
Exponential Smoothing (ES) Techniques

## Slide 11
Iterative reweighted least-square [1]
Autocorrelation and Partial Autocorrelation function of resulting immediate past load data
Thus identifies a sub-optimal model of the load projection
Time Space
Simple
Box-Jenkins
Frequency Space
Fourier Analysis
Harmonic Regression
Phase Space
Artificial Intelligence (AI)
Regression
State Space
Non linear dynamics
Chaos Theory
Modern Approach
Kalman Filters
Sequential Monte-Carlo Filters
Data Mining
Stochastic Time Series Methods [1], [5], [7]
Based on the assumption that data have an internal structure like trends or autocorrelation
Based on the previous load data (historical)
Auto Regressive (AR) Model [1], [5], [7]
Current value of series 𝑦𝑡 expressed as a linear combination of previous/past loads to forecast future load values
A 𝑝th order AR model, AR(𝑝) is
yt - yt-i = 𝜀𝑡
ϕ1, ϕ2,… ϕp are unknown AR coefficients
𝜀𝑡 is random white noise
Correlation needed between current values of 𝑦𝑡 and its past values
Applied in economics electric load forecasting and digital signal processing
Auto Regressive (AR) Model [1], [5], [7]
Current value of series 𝑦𝑡 expressed as a linear combination of previous/past loads to forecast future load values
A 𝑝th order AR model, AR(𝑝) is
yt - ∑_(𝒊=𝟏)^𝒑▒𝝓_𝒊 yt-i = 𝜀𝑡
ϕ1, ϕ2,… ϕp are unknown AR coefficients
𝜀𝑡 is random white noise
Correlation needed between current values of 𝑦𝑡 and its past values
Applied in economics electric load forecasting and digital signal processing
Moving Average (MA) Model [1], [5], [7]
Mimics behavior of a MA process
Linear regression model that regresses current values against white noise of one or more past values
Time series regarded as a MA of a (unevenly weighted) random shock series 𝜀t
MA model of order 𝑞 MA(𝑞) is given as
yt = 𝜀𝑡 + t-i
Duality/Invertibility between MA and AR model
MA model can be rewritten (inverted) into an AR form (of infinite order)
Moving Average (MA) Model [1], [5], [7]
Mimics behavior of a MA process
Linear regression model that regresses current values against white noise of one or more past values
Time series regarded as a MA of a (unevenly weighted) random shock series 𝜀t
MA model of order 𝑞 MA(𝑞) is given as
yt = 𝜀𝑡 + ∑_(𝒊=𝟏)^𝒒▒〖Ɵ_𝒊 "𝜀" 〗t-i
Duality/Invertibility between MA and AR model
MA model can be rewritten (inverted) into an AR form (of infinite order)

## Slide 12
Auto Regressive Moving Average (ARMA) Model [1], [5], [7]
Combination of an AR models AR(𝑝) and MA models MA(𝑞)
Express current value 𝑦𝑡 linearly in terms of its past values and current, previous values of the noise
Mathematically ARMA(𝑝,𝑞) model is written as yt - yt-i = 𝜀𝑡 + t-i
Relatively simple and effective
Auto Regressive Moving Average (ARMA) Model [1], [5], [7]
Combination of an AR models AR(𝑝) and MA models MA(𝑞)
Express current value 𝑦𝑡 linearly in terms of its past values and current, previous values of the noise
Mathematically ARMA(𝑝,𝑞) model is written as yt - ∑_(𝒊=𝟏)^𝒑▒𝝓_𝒊 yt-i = 𝜀𝑡 + ∑_(𝒊=𝟏)^𝒒▒〖Ɵ_𝒊 "𝜀" 〗t-i
Relatively simple and effective
ARMAX & ARIMAX Models (with exogenous inputs) [1], [5], [7]
Loads depend on weather, time etc. given as exogenous variables
Current value of time series 𝑦𝑡 is expressed linearly in terms of its past values, current and previous values of noise and in terms of present and past values of the exogenous variables
The ARMAX(𝑝, 𝑞, 𝑟1, … … , 𝑟𝑘) is given as
ϕ(𝐵).𝑦𝑡 = θ(𝐵). 𝜀𝑡 + i(B).vti
where the 𝑟i’s are the orders of the exogenous factors (variables)
𝑣𝑡𝑖 and 𝜓𝑖(B) is a shorthand notation for
𝜓𝑖(B) = (𝜓0𝑖 + 𝜓1𝑖.B + ⋯ + 𝜓𝑟𝑖i .𝐵𝑟i )
with the 𝜓𝑗𝑖’s being the corresponding coefficients
ARMAX & ARIMAX Models (with exogenous inputs) [1], [5], [7]
Loads depend on weather, time etc. given as exogenous variables
Current value of time series 𝑦𝑡 is expressed linearly in terms of its past values, current and previous values of noise and in terms of present and past values of the exogenous variables
The ARMAX(𝑝, 𝑞, 𝑟1, … … , 𝑟𝑘) is given as
ϕ(𝐵).𝑦𝑡 = θ(𝐵). 𝜀𝑡 + ∑_(𝒊=𝟏)^𝒌▒𝜳i(B).vti
where the 𝑟i’s are the orders of the exogenous factors (variables)
𝑣𝑡𝑖 and 𝜓𝑖(B) is a shorthand notation for
𝜓𝑖(B) = (𝜓0𝑖 + 𝜓1𝑖.B + ⋯ + 𝜓𝑟𝑖i .𝐵𝑟i )
with the 𝜓𝑗𝑖’s being the corresponding coefficients
AR Integrated MA (ARIMA) Model [1], [5], [7]
AR, MA, or ARMA are suitable for stationary time series data
So ARIMA is for business & economic non-stationary behavior
(i) AR parameters (ϕ1, ϕ2,…ϕp) (ii) MA parameters (θ1, θ2,…θ𝑞) and (iii) number of differencing (d) conducted to (1- B)
where B represents a lag operator
Seasonal variants of ARIMA are SARIMA models
Generalized as AR Fractionally Integrated MA (ARFIMA) model allows non-integer values of differencing parameter 𝑑
ARFIMA models time series with a long memory
Random noise disturbs the whole process
AR Integrated MA (ARIMA) Model [1], [5], [7]
AR, MA, or ARMA are suitable for stationary time series data
So ARIMA is for business & economic non-stationary behavior
(i) AR parameters (ϕ1, ϕ2,…ϕp) (ii) MA parameters (θ1, θ2,…θ𝑞) and (iii) number of differencing (d) conducted to (1- B)
where B represents a lag operator
Seasonal variants of ARIMA are SARIMA models
Generalized as AR Fractionally Integrated MA (ARFIMA) model allows non-integer values of differencing parameter 𝑑
ARFIMA models time series with a long memory
Random noise disturbs the whole process

## Slide 13
Kalman Filtering Algorithm [5]
efficient computational (recursive) means to estimate state of an observed process
Applied in Tracking, motion prediction & for multi-sensor (inertial-acoustic) fusion
Complex factors are given as inputs while weather and time factors are included in the KF
discrete-time linear dynamic system with a set of mathematical equations in state space
Works in two steps (i) Predictor and (ii) Corrector
Non linear variants are Extended KF and Unscented KF
Grey Models
Grey System Theory (GST) [5]
GM(1,1) produces forecasts of the future primitive data points
Time series model with differential equation (DE) having time-dependent varying coefficients
Accumulated Generation (AG) smoothens and lowers the intensity of uncertainty in system
Used for exponential growth trend problems in short, medium & long term forecasts
Deals with systems that have partially unknown parameters
Estimation of unknown system behavior with limited data
Solving DE, n-step predicted value of system can be obtained
Inverse AG (IAG) can be applied to extract the predicted values of the original data
Load distribution and load trend need not be considered
Use random variations as grey quantity which changes in certain interval

## Slide 14
Fuzzy Logic [1], [5]
Generalization of Boolean theory by associating inputs with specific qualitative ranges
Wavelet Neural Networks (WNN) [1], [5], [7]
WNN takes advantage of both wavelet functions and neural network
Useful for handling uncertainties and for knowledge acquisition of human experts
Membership function can be represented for every fuzzy set which exhibits a specific continuous curve that is changing from 0 to 1 or vice versa, while a corresponding transition’s region represents a fuzzy boundary of the term
Combined with other methods to achieve good prediction results
Used in cases where mathematical models are not appropriate to use
Appropriate for systems having uncertainties in either their inputs or definition and are too complicated or non-linear
Alternative to FFANNs for approximating arbitrary nonlinear functions by means of a wavelet transform theory
WNN takes wavelet space in spirit of feature space for pattern recognition
Feature extraction of signal by calculating internal product of wavelets base and signal vector
Learns input and output characteristics of system without too much prior information
Signal is transmitted forward and error is proliferated backward acquiring accurate predictive values
Robust for approximating non-linear functions

## Slide 15
Regression and classification mechanisms developed to deal with pattern classification problems like face identification, optical recognition etc.
Deducts a specific decision rule by choosing some specific subset of training data, called support vectors
Nonlinear mapping of input space into a higher dimensional feature space
Complexity and quality of solutions do not depend on the input space
VM solutions appear to be always globally optimal and unique
SVMs based on PSO are suitable for short-term load forecasting
Requires huge computations so time complexity of the solutions is high
Support Vector Machines (SVM) [5]

## Slide 16
xj1
b1
xj2
xjk
xjn-1
xjn
b2
bk
bL
bL-1
Inputs
tj = ŷj
Desired output
Input Layer
Hidden Layer
Output Layer
Weights in the input layer
Weights in the output layer
Special class of Feed Forward ANNs appropriate for regression, classification, clustering, feature learning, and sparse approximation
Address a single-hidden layer FF neural network
Weights of hidden layer nodes are randomly selected, and a least-squares solution can analytically determine the output weights of ELM
Hidden nodes can be randomly allocated and, afterward, never updated
Output weights of the hidden nodes are settled in a single step which decreases learning time of ANN
Outperform support vector machines, which provide sub-optimal solutions in both regression and classification problems
Extreme Learning Machines (ELM) [5]

## Slide 17
Genetic Algorithms (GA)
Developing a solution with help of operators mimicking genetic variation
Population composed of individuals with specific selection rules
Population of individuals maximize success of solution & minimize cost
Heuristic or metaheuristic method based on survival of the best
Optimization based on natural selection from various models’ candidate population; Also suitable for non linear systems
A fitness function for optimization
The function GA is trying to optimize
Chromosome population (refers to values that represent candidate solution to problem)
randomly chosen set of chromosomes serve as initial population (1st gen)
Chromosome reproducibility based on probability distribution defined by user
Biological crossover & recombination in cell meiosis to reproduce
Random mutation in new generation flips individual bits in new chromosomes
Evaluated by fitness function to test solvability of population
Genetic Algorithms [5]

## Slide 18
Expert System Based
New techniques based on AI
Computer program with ability to reason, explain & expand knowledge
Knowledge component is extracted from experts in field & coded into IF-THEN statements
Some rules do not change over time while some get updated continuously
Changes in system load vs changes in exogenous factors affecting load
Combines rules & procedures used by human experts
Changes in system load vs changes in natural, forced condition factors that effect use of electricity
Rule base is used for daily forecast generation
Expert System Based [1], [5]

## Slide 19
Scenario based Approach
Forecasts based on plausible scenarios & has low probability of occurrence
Wide range of forecasts are possible with attaining extremes too
Scenarios are generated by considering all possible factors or drivers, their relative impacts, interactions between them with involvement of decision makers
Many scenarios will be generated but only best, middle and worst are presented
Documenting contrasting extremes will help in contingency planning
Development of conceptual scenario of future based on well defined set of assumptions
Plausible scenarios capture structural changes, emergence of new economic activities or disappearance of activities
Decision maker determines which scenario is most likely to occur in future and makes decision accordingly
Scenario Based Approach [6]

## Slide 20: Artificial Neural Network [1], [2], [5], [7]
Alternative mechanism to Time series model
Forecasting & classification purposes since 1990
Neural Network is a non linear circuit which does non linear curve fitting
Information processing paradigm inspired by functioning of human brain
Recognizes regularities and patterns in input data & learns from experience
Composed of several interconnected Processing Elements (PE) called neurons
Neurons change their dynamic state response with respect to external inputs
Simplest form of ANN contains input, hidden and output layers
Input node
𝐼=∑24_(𝑖=1)^𝑁▒〖𝑤_𝑖 𝑥_𝑖 〗
Hidden node
Y = f(x).I
Input node
Hidden node
Y = f(x).I
wnew = wold + δ.ɣ.x
Delta Rule
Output node
x
y
f(x)
Simple neuron scheme in an ANN

## Slide 21
ANN algorithms for ELF [1], [2], [5], [7]
Feed Forward
NARX (Non linear)
Back Propagation
Radial Basis Function (RBF)
Random
Recurrent
Self organizing
ANN [1], [2], [5], [7]
1st group
Only one output node
Next day’s peak or total and next hour’s load etc.
2nd group (strong robustness and learning ability)
Multiple output nodes (typically 24)
Sequence of hourly loads (next day’s load profile)
Preferred output from a specific input achieved by changing weights of NNs
Changing weights of NNs is called iterative training process
Learning convergence speed is low
Restriction on generalization ability & quickly falls into local minima
NARX networks together with RBF networks possess simplicity, reliability, low % error, high accuracy and handle nonlinearity of variables

## Slide 22
Hybrid Approach
Better performance than single models
Integrates advantages of single models
Combines econometric & engineering models
Numerous techniques & algorithms available
No proper references to build hybrid models
Best statistical & machine learning models
Statistical methods effective with limited data availability counteract extensive data requirements of machine learning methods
Prior knowledge reduces computational effort
Incorporates cross-learning, a capability that many statistical methods lack
Solution to dilemma of assumption of linearity
Effective in real world cases where traditional approaches are not
Hybrid Approach [5], [6]

## Slide 23
Energy Demand Analysis
Determines if the proposed energy mix is compatible with sustainable goals & projected energy demand levels
Macro­economic developments vs energy needed to sup­port those developments in each sector
Enables a disaggregated, end use approach to analyze the energy requirements
Considers the activities in individual energy­ consuming sectors of the economy
Uses economic, demographic and energy use information to compute and report on consumption of end use fuels
Output of database establishment serves as input to energy policy analysis facilitating iterative demand analysis
Plays a sequential, intermediate, and iterative role in energy planning
Approaches of Energy Demand Analysis
Macro Analysis
Considers demand as a function of popula­tion, income, and prices
Examines structure of sectors and sub-sectors and their energy consuming activities
Sectoral Analysis
Energy Demand Analysis[8], [9]

## Slide 24
Issues of Energy Demand Analysis [8], [9]
Energy planning exercises are carried out with aggregate data at national level only
Energy resources and demand are spatially distributed
To meet basic energy needs of population at a reasonable cost would be an important policy ob­jective
Impact of shortages on outputs of various sectors like agriculture, industry etc.
Studies of traditional fuel sources are needed to focus on issues eg.Biomass handling
Analysis of various methods of estimating energy shortages or unfulfilled demand for different sec­tors and categories of consumers
Estimates should be made of energy shortages and the processes through which the shortages have been managed
Need to evaluate social profitability of the allocation of various scarce resources to conserve rather than augment

## Slide 25: References
[1] Hesham K. Alfares and Mohammad Nazeeruddin.,Electric Load Forecasting: literature survey and classification of methods,
International Journal of Systems Science, 2002, Volume 33, Number 1, Pages 23 – 34
[2] Tahreem Anwar, Bhaskar Sharma, Koushik Chakraborty and Himanshu Sirohia.,Introduction to Load Forecasting.,
International Journal of Pure and Applied Mathematics Volume 119 No. 15 2018, 1527-1538
[3] George E. Oamek, Burton C. English., A Review of Load Forecasting Methodologies., IOWA State University CARD
Working Papers
[4] Shalabh., Econometrics - Chapter 1 : Introduction to Econometrics., , IIT Kanpur
[5] Mahmoud A. Hammad, Borut Jereb, Bojan Rosi, Dejan Dragan., Methods and Models for Electric Load Forecasting: A
Comprehensive Review., Logistics and Sustainable Transport Vol. 11, No. 1, February 2020, 51-76
[6] Central Electricity Authority., Long Term Electricity Demand Forecasting.,
[7] Adebayo Adeniyi D, Emu Chuks., Long Term Electric Load Forecasting for Bonny and Finima Towns using Linear
Regression Method. International Journal of Engineering Research and Technology (IJERT) Vol. 8 Issue 11, November-
2019
[8] W. Ganapini., Energy Demand Analysis as a Planning Instrument in Limited Resources Areas: the Enza River Valley Case.
Energy for Rural and Island Communities, Proceedings of the Second International Conference, Held at Inverness,
Scotland, 1–4 September 1981-1982, Pages 63-69
[9] T. V. Ramachandra, S. Vamsee Krishna and B. V. Shruthi., Decision Support System for Regional Domestic Energy
Planning. Energy Research Group, Centre for Ecological Sciences, Indian Institute of Science, Bangalore 560 012