## Slide 1: MALAVIYA NATIONAL INSTITUTE OF TECHNOLOGY JAIPUR CENTRE FOR ENERGY AND ENVIRONMENT RET 615 SEMINAR End Term Examination – 13.12.2021
Impact Analysis of Short Term Power Procurement Planning for Renewable Energy rich DISCOMs
Presented by
Bala Ganesh K
2020PCV5316
Supervisor
Dr. Parul Mathuria
Assistant Professor

## Slide 2
CONTENTS
2
Significance
Indian DISCOMs Overview
Future Scope
Impact Analysis - Methodology
RE Integration & Long Term PPAs
References
Indian Power Sector Overview
Short Term Procurement - Market Mechanisms
Results and Discussion
Power Procurement – Indian Scenario

## Slide 3
SIGNIFICANCE
3
POLLUTION
GLOBAL WARMING
EXHAUSTIBLE FUELS
GRID SCALE
CAPACITY UTILIZATION
UNCERTAIN DEMAND
INEXHAUSTIBLE
CLEAN
NO COST FUEL
INTERMITTENT
GEO - AVAILABILITY
INTEGRATION
CAPACITY ADDITION
SOCIO - ECONOMIC
POLICY DECISIONS
MARKET MECHANISMS
RISK OF UNCERTAIN PRICES
DISCOM SPECIFIC
[1], [5], [10]
[10], [12], [16]

## Slide 4
Central
State
Private (CPP/IPP)
GENERATING COMPANIES
TRANSMISSION COMPANIES
DISTRIBUTION COMPANIES
CONSUMER/LOAD
Direct sale
PPAs with Discoms
Market sale
Day Ahead Market
Open Access for large consumers
Term Ahead Market
Real Time Market
Transmission capacity & allocation priority
Transmission charges & waive off for RES
Green corridors for RES generation evacuation
Own Generation
Purchase and Sale
24*7 Power for all
RPO
Short Term Markets
From Discoms
Open Access
Roof Top Solar PV
Reliability & Quality
Cost effective power
INDIAN POWER SECTOR OVERVIEW [6], [19]
4
GOVERNMENT & REGULATORS

## Slide 5
INDIAN DISCOMs OVERVIEW
5
Power Purchase Agreements [1, 25]
Long term (12-25 years)
Medium term (1-12 years)
Market based Power Purchase [8, 16]
Day Ahead Market
Green - DAM
Real Time Market
Short term (less than 1 year)
REC Market
ESCERTS Market
Term Ahead Market
Green - TAM
Very Short Term (Intra day)
Levelized Cost Of Electricity
Aggregate Revenue Requirement (ARR)
Per unit cost of electricity
Generation cost
Landed Cost (Evacuation)
ARR for DISCOMs
Consumer bill
FINANCIAL ASPECTS [7], [14]
High Subsidies without financial back up from State Govt.
Non Liquidation of Regulatory Assets
High Aggregate Technical and Commercial Loss
Customers opting Open Access & Behind The Meter generation

## Slide 6
POWER PROCUREMENT – INDIAN SCENARIO [6], [8], [10], [14], [18], [19]
6

## Slide 7
RENEWABLE ENERGY INTEGRATION
7
WIND ENERGY
SOLAR ENERGY
HYDRO ENERGY
FACTORS
[5], [10], [11], [12]
Load profile & load duration profile
Existing Long term & medium term contracts
Intra state transmission network
Own generation
Energy Market Contracts
Share of RES (FIT contracts & RPO)
[5], [10], [11], [12]
IMPACTS
[5], [10], [11], [12]
Demand variation
RES Integration
Optimum generation mix
Reduce gap between ACS-ARR
Consumer Financial benefits
Transmission capacity addition

## Slide 8
RENEWABLE ENERGY INTEGRATION & LONG TERM PPAs
8
TAMIL NADU - RENEWABLE GENERATION ESTIMATION [2], [17], [20]
Chart: Solar Generation Data
| 00:30:00 | 01:30:00 | 02:30:00 | 03:30:00 | 04:30:00 | 05:30:00 | 06:30:00 | 07:30:00 | 08:30:00 | 09:30:00 | 10:30:00 | 11:30:00 | 12:30:00 | 13:30:00 | 14:30:00 | 15:30:00 | 16:30:00 | 17:30:00 | 18:30:00 | 19:30:00 | 20:30:00 | 21:30:00 | 22:30:00 | 23:30:00
January (17) | 0 | 0 | 0 | 0 | 0 | 0 | 165240.161 | 779946.852 | 1354777.619 | 1772789.369 | 2029331.716 | 2117909.816 | 2067972.911 | 1875731.689 | 1525426.834 | 1033837.05 | 423902.07 | 10228.719 | 0 | 0 | 0 | 0 | 0 | 0
February (16) | 0 | 0 | 0 | 0 | 0 | 0 | 232363.782 | 835771.549 | 1411485.788 | 1807536.189 | 2036010.115 | 2087960.67 | 2043260.588 | 1862901.269 | 1520673.929 | 1045560.308 | 455256.419 | 20351.065 | 0 | 0 | 0 | 0 | 0 | 0
March (16) | 0 | 0 | 0 | 0 | 0 | 0 | 265967.898 | 901172.37 | 1477994.743 | 1869730.531 | 2101505.897 | 2193261.62 | 2145536.722 | 1966608.682 | 1655493.516 | 1192031.076 | 601099.452 | 62897.787 | 0 | 0 | 0 | 0 | 0 | 0
April (15) | 0 | 0 | 0 | 0 | 0 | 908.616 | 337997.548 | 915327.625 | 1418212.845 | 1786236.359 | 2007752.37 | 2099300.315 | 2058179.688 | 1889563.965 | 1598510.347 | 1164028.3 | 618317.962 | 89368.598 | 0 | 0 | 0 | 0 | 0 | 0
May (15) | 0 | 0 | 0 | 0 | 0 | 1891.274 | 175497.343 | 482029.999 | 795468.725 | 1065129.46 | 1236840.688 | 1490558.387 | 1590279.807 | 1519658.419 | 1250946.823 | 866585.282 | 405433.112 | 52604.87 | 0 | 0 | 0 | 0 | 0 | 0
June (11) | 0 | 0 | 0 | 0 | 0 | 8506.476 | 249126.813 | 601926.795 | 951226.541 | 1212318.014 | 1391163.503 | 1495344.251 | 1486512.532 | 1376747.962 | 1151049.261 | 796499.555 | 437588.375 | 101703.182 | 0 | 0 | 0 | 0 | 0 | 0
July (17) | 0 | 0 | 0 | 0 | 0 | 7045.936 | 242409.144 | 589773.293 | 919961.58 | 1251465.978 | 1551872.264 | 1689513.185 | 1551765.638 | 1308760.117 | 860168.558 | 518489.408 | 237078.512 | 37302.65 | 0 | 0 | 0 | 0 | 0 | 0
August (16) | 0 | 0 | 0 | 0 | 0 | 0 | 134211.465 | 430637.817 | 738290.374 | 975030.007 | 1166648.004 | 1335340.996 | 1416709.615 | 1267540.408 | 812701.974 | 480543.505 | 204085.896 | 22831.378 | 0 | 0 | 0 | 0 | 0 | 0
September (15) | 0 | 0 | 0 | 0 | 0 | 0 | 119509.472 | 443898.474 | 914533.209 | 1332474.077 | 1480454.335 | 1447357.668 | 1411169.179 | 1320453.828 | 1127091.292 | 724437.297 | 304829.424 | 24665.683 | 0 | 0 | 0 | 0 | 0 | 0
October (15) | 0 | 0 | 0 | 0 | 0 | 0 | 75465.746 | 315806.43 | 555213.587 | 761192.146 | 904044.163 | 1019567.766 | 1064755.672 | 965359.646 | 739658.039 | 408206.968 | 178729.704 | 7536.251 | 0 | 0 | 0 | 0 | 0 | 0
November (14) | 0 | 0 | 0 | 0 | 0 | 0 | 159240.457 | 702954.905 | 1356462.57 | 1763482.625 | 1998194.305 | 2049468.595 | 2000366.008 | 1831679.817 | 1511871.128 | 972912.899 | 403407.898 | 13215.455 | 0 | 0 | 0 | 0 | 0 | 0
December (10) | 0 | 0 | 0 | 0 | 0 | 0 | 125194.203 | 670396.163 | 1226133.147 | 1610019.357 | 1841407.141 | 1928772.98 | 1879466.048 | 1701230.616 | 1362398.598 | 811597.347 | 349888.765 | 5945.539 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Wind Generation Data
| 00:30:00 | 01:30:00 | 02:30:00 | 03:30:00 | 04:30:00 | 05:30:00 | 06:30:00 | 07:30:00 | 08:30:00 | 09:30:00 | 10:30:00 | 11:30:00 | 12:30:00 | 13:30:00 | 14:30:00 | 15:30:00 | 16:30:00 | 17:30:00 | 18:30:00 | 19:30:00 | 20:30:00 | 21:30:00 | 22:30:00 | 23:30:00
January (17) | 2997555.6 | 2966710.657 | 2781796.164 | 2389824.061 | 1978872.584 | 1688157.016 | 1350772.578 | 1254145.971 | 2704218.335 | 2553870.099 | 2289795.894 | 2103579.373 | 1970599.213 | 1894240.163 | 2092964.523 | 2660202.081 | 3443164.079 | 4839056.62 | 5351197.857 | 4843183.305 | 4351735.807 | 3662353.675 | 2962914.361 | 2476515.086
February (16) | 417915.492 | 113977.083 | 29431.011 | 69545.626 | 156824.961 | 178180.972 | 62474.402 | 7725.699 | 5123.14 | 4829.531 | 9805.473 | 28390.047 | 67876.998 | 137863.693 | 244521.725 | 485000.681 | 1230486.338 | 3771484.943 | 5457756.904 | 5675039.603 | 4403596.318 | 2300503.459 | 899912.643 | 258637.33
March (16) | 980392.714 | 575302.47 | 350072.09 | 283753.412 | 289625.055 | 267089.286 | 236697.438 | 375103.145 | 632506.725 | 899815.329 | 1051341.189 | 1246362.117 | 1544233.593 | 1964607.287 | 2426103.013 | 2997444.665 | 3886280.358 | 4996747.738 | 5214697.314 | 4542520.552 | 3746649.974 | 2962845.105 | 2413694.841 | 1932852.501
April (15) | 821431.571 | 522696.36 | 277160.488 | 122000.52 | 42514.667 | 9253.548 | 13622.174 | 122046.629 | 96174.392 | 81524.316 | 97156.487 | 124826.973 | 173833.192 | 267068.351 | 445616.828 | 746095.919 | 1403730.998 | 3311978.042 | 5680552.489 | 5296984.909 | 4357104.225 | 2637873.529 | 1758489.057 | 1478256.28
May (15) | 259121.351 | 40385.882 | 2134.154 | 580.154 | 75.124 | 1861.445 | 58184.433 | 275698.339 | 217898.742 | 115490.425 | 74807.17 | 81441.015 | 99963.352 | 111006.536 | 94565.585 | 59289.246 | 20671.147 | 9300.311 | 29710.522 | 331469.87 | 811550.868 | 1076303.991 | 1006175.772 | 811122.451
June (11) | 1790973.93 | 1811003.756 | 1786188.62 | 1562830.702 | 1355346.754 | 1274919.309 | 1646050.267 | 2955252.906 | 3955234.265 | 4256989.527 | 4421922.4 | 4739561.055 | 5284786.292 | 5928789.04 | 6641887.294 | 7234242.841 | 7448421.553 | 7238081.919 | 6739743.667 | 5505064.846 | 4698043.315 | 3996615.513 | 3151263.086 | 2561581.028
July (17) | 2758178.15 | 2682164.811 | 2536593.749 | 2437353.52 | 2370144.991 | 2135454.255 | 3229857.041 | 4581054.122 | 3826055.616 | 2454330.192 | 1401475.041 | 843965.594 | 585282.589 | 435302.885 | 428412.81 | 566935.13 | 843278.197 | 1240978.005 | 1625402.964 | 1851841.35 | 1888268.492 | 3031798.447 | 3175602.725 | 3335667.771
August (16) | 2846958.865 | 2576203.752 | 1875538.713 | 1407772.281 | 1155648.483 | 958939.333 | 1217965.356 | 3210804.594 | 4251803.569 | 4067328.872 | 3722777.084 | 3568815.735 | 3527564.625 | 3161858.623 | 2509034.921 | 2135079.838 | 1979095.001 | 1979131.666 | 2077295.469 | 1998417.153 | 2084315.76 | 1894252.002 | 1499126.682 | 1242399.702
September (15) | 2510553.751 | 2552757.652 | 2320362.185 | 1981495.326 | 1662356.695 | 1533403.323 | 1179098.349 | 899738.635 | 1485824.239 | 1386515.344 | 1086388.992 | 855247.886 | 668884.998 | 551837.278 | 554897.972 | 681332.624 | 744895.361 | 817895.328 | 1074240.07 | 1249596.259 | 1282442.047 | 1520753.854 | 1855891.21 | 2190217.686
October (15) | 573564.525 | 478390.849 | 387475.062 | 266902.754 | 203670.895 | 228872.99 | 346183.561 | 302710.688 | 461815.3 | 613785.808 | 605076.181 | 588893.526 | 628739.672 | 601697.481 | 573684.731 | 523689.968 | 540063.079 | 702870.423 | 942964.998 | 1195621.712 | 1308198.863 | 1259367.808 | 1104197.681 | 990185.448
November (14) | 1506872.901 | 1666071.663 | 1662151.393 | 1705084.559 | 1686426.81 | 1593662.922 | 1089531.806 | 773080.096 | 1520166.433 | 1790449.713 | 1866743.738 | 1912788.842 | 1998238.321 | 2135082.857 | 2155533.974 | 2142266.131 | 1979933.996 | 1947828.828 | 2131311.138 | 2027415.589 | 1864454.625 | 1654174.246 | 1412554.246 | 1215796.741
December (10) | 2634535.684 | 2674269.969 | 2711995.185 | 2566046.11 | 2308881.732 | 2276977.802 | 2154944.289 | 1061354.478 | 2183452.747 | 3063897.028 | 2838184.57 | 2431523.319 | 2155288.25 | 2048167.138 | 2123308.059 | 2319265.041 | 2373850.786 | 2917321.834 | 3581440.054 | 3476669.483 | 3448976.284 | 3386192.222 | 3270706.271 | 3312083.84
Wind 9628 MW
Bio power and Cogeneration 1019 MW
Solar Rooftop 325 MW
Small Hydel
123 MW
Solar Ground Mounted 4150 MW
Large Hydro 2178 MW
Source: www.renewablesindia.in – CEA/CEEW/CEF
Installed RE Capacity - April 2021
Source: www.renewablesindia.in – CEA/CEEW/CEF and www.renewableninja.com
ISGS (Central Thermal, Central Nuclear & Other Thermal)
Renewable (Wind, Biomass, Bagasse & Solar) & Traders
Market Procurement (Bilateral Contracts, DAM, RTM)
State (Thermal, Hydro & Gas) & Long Term PPAs
Behind the Meter Generation (PROSUMERS)
POWER PROCUREMENT EVOLUTION [2], [13], [14]

## Slide 9
SHORT TERM PROCUREMENT - MARKET MECHANISMS
9
INDIAN ELECTRICITY MARKET [5], [8], [16]
BILATERAL CONTRACTS
EXCHANGES
SECURITY CONSTRAINED ECONOMIC DISPATCH
Day Ahead Market
Term Ahead Market
Real Time Market
Renewable Energy Certificates Market
DEMAND FORECASTING (TIME SLOT)
IDENTIFICATION OF SOURCES/SUPPLIERS
TECHNICAL & FINANCIAL CONSIDERATIONS
NEGOTIATION OF T&C : ESTABLISHMENT OF CONTRACTS
EVALUATION OF CONTRACTS AND RECEIVE SUPPLY
MARKET PROCUREMENT [5], [8], [16]
Green Day Ahead Market
Green Term Ahead Market

## Slide 10
IMPACT ANALYSIS - METHODOLOGY
10
Demand Data & Renewable Generation  Input to model
GAMS Model  Cost optimization & Risk Analysis
API Software  GUI development (FUTURE SCOPE)
Mathematical Model  Constraints & Power Balance
Input from MS Excel
Conventional Generation details
Diurnal load demand
PV Generation data
Wind Generation data
Hydro Generation data
Market Details
{DAM RTM REC}
SIMPLE COST OPTIMIZATION
Preliminary Economic Dispatch
Economic Dispatch with PV & Wind
COST OPTIMIZATION WITH MARKET INTEGRATION
Market procurement (DAM, RTM, G-DAM)
DSM & RPO Constraints
Risk analysis of Uncertainty in MCP

## Slide 11
MATHEMATICAL MODEL
11
Final cost, CFINAL = CTOTAL + [α*Risk]
where,
CFINAL  Total cost incurred to DISCOM at various levels of risk taking scenario with market clearing price uncertainty
CTOTAL  Cost of procuring power at maximum risk of market clearing price uncertainty
Risk  Uncertainty in market clearing prices of DAM, RTM and DSM price based on real time grid frequency
α Risk weighing factor, which when increases indicates lesser willingness to take risk
Objective Function
Total cost, CTOTAL = CC + CH + CLS + CDSM + CPX + CDAM + CRTM + CG_DAM + CS_REC + CNS_REC
where,
CC  Conventional generation cost CDAM  Cost of procurement from DAM
CH  Hydro generation cost CRTM  Cost of procurement from RTM
CLS  Penalty cost for Load Shedding CG_DAM  Cost of procurement from G_DAM
CDSM  Cost for deviation from schedule CS_REC  Cost of procuring Solar REC
CPX  TAM contracts procurement cost CNS_REC  Cost of procuring Non Solar REC
Procurement Cost modelling

## Slide 12
MATHEMATICAL MODEL
12
Risk = DSMvar (PtDSM)2 + DAMvar(PtDAM)2 + RTMvar(PtRTM)2 + 2{covar1(PtDSM *PtDAM) +
covar2(PtDSM *PtRTM) + covar3(PtDAM *PtRTM)}
where,
t  time block of 15 minutes
λtDSMvar Variance of DSM price in last 30 days based on changing real time grid frequency
λtDAMvar Variance of DAM clearing price in last 30 days
λtRTMvar Variance of RTM clearing price in last 30 days
λtcovar1 Co-variance between DAM clearing price and DSM rate in last 30 days
λtcovar2 Co-variance between RTM clearing price and DSM rate in last 30 days
λtcovar3 Co-variance between DAM clearing price and RTM clearing price in last 30 days
PtDSM Power deviated from scheduled drawl
PtDAM Power procured through DAM
PtRTM Power procured through RTM
Risk modelling of uncertainties in price [27]

## Slide 13
MATHEMATICAL MODEL
13
Power balance
+ + + + + + + = - -
where,
 Power demand in MW
 Solar power output available in MW
 Wind power output available in MW
min*ut < < max*ut
min*uht < < max*uht
*ut - *ut-1 < *ut
*ut-1 - *ut < *ut-1
ut > utt – utt-1 , when [ tt > t – UT ]
1-ut > utt-1 – utt , when [ tt > t – DT ]
Constraints
*uht - *uht-1 < *uht
*uht-1 - *uht < *uht-1
< 0.12*[]
+ ] = max * pt * Px_avail
[S_RPO* ] < + S_REC +
[NS_RPO* ] < + NS_REC +

## Slide 14
RESULTS AND DISCUSSION
14
Chart: Inputs - July
Chart: Inputs - March
Chart: Uncertainties - November
Chart: Uncertainties - March
TAMIL NADU – HIGH RE SCENARIO
RAJASTHAN – HIGH RE SCENARIO
WITH G_DAM – LOW RE SCENARIO
WITHOUT G_DAM – HIGH RE SCENARIO

## Slide 15
RESULTS AND DISCUSSION
15
TAMIL NADU – HIGH RE SCENARIO – LOW RISK
TAMIL NADU – HIGH RE SCENARIO – HIGH RISK
Chart: Power Procurement Portfolio – July (Low Risk)
Chart: Power Procurement Portfolio – July (High Risk)
THERMAL
NUCLEAR
CONTRACTS
RENEWABLES
DSM
STM

## Slide 16
RESULTS AND DISCUSSION
16
Chart: Risk Analysis - July
| 165.762 | 165.86699999999999 | 166.041 | 168.804 | 174.28200000000001 | 175.58199999999999 | 175.709
 | 69744460 | 69696780 | 69417710 | 24197600 | 1820791.32 | 1290766.06 | 1214819.912
Chart: Risk Analysis - November
| 174.09 | 177.49799999999999 | 183.553 | 183.596
 | 4893406.658 | 857340.503 | 95995.602 | 29423.472
TAMIL NADU – LOW RE SCENARIO
TAMIL NADU – HIGH RE SCENARIO
TAMIL NADU – LOW RE SCENARIO
Chart: Power Procurement Portfolio - November

## Slide 17
RESULTS AND DISCUSSION
17
RAJASTHAN – LOW RE SCENARIO
RAJASTHAN – HIGH RE SCENARIO
Chart: Power Procurement Portfolio - March
Chart: Power Procurement Portfolio - November

## Slide 18
RESULTS AND DISCUSSION - COMPARISON
18
Chart: High RE Scenario with Demand
Chart: RES Curtailment
Chart: Short Term Market Procurement
Chart: Green DAM Procurement

## Slide 19
RESULTS AND DISCUSSION – COMPARISON & IMPLICATIONS
19
Chart: DSM drawl – Tamil Nadu
Chart: DSM drawl - Rajasthan
Long Term Impacts
Operational reliability
Inertia availability for frequency response
Long term policy framework
Procurement Portfolio design
Short Term Impacts
Real power balancing
Increased Reserve requirement
RE curtailment minimization
Scheduling of conventional power plants
TECHNICAL
Reserve Requirements (Frequency & Voltage)
Ramping Requirements & Transmission Congestion
FINANCIAL
RPO, RGO & DSM
Tariff Philosophy, Green Energy Markets
POLICY AND REGULATION
INFRASTRUCTURE
Uncertainty of Market Clearing Price
ACS – ARR of DISCOMs & Impact of OA consumers
Capacity Addition Planning & Storage Requirements
Metering & ICT Requirements

## Slide 20
RESULTS AND DISCUSSION – COST COMPARISON
20
PROCUREMENT COST SUMMARY |  |  | PROCUREMENT COST SUMMARY | 
State | RE availability | Risk | Procurement Cost per day (Crores) | Annual Procurement Cost (Crores)
Tamil Nadu | High | High | 165.70 | 72,462.40
 | High | Low | 175.70 | 76,118.30
 | Low | High | 176.93 | 77,857.70
 | Low | Low | 183.20 | 79,060.20
Rajasthan | High | - | 108.62 | 57,957.88
 | Low | - | 142.08 | 70,407.56
Chart: Procurement Cost – Per Day
| Procurement Cost per day (Crores)
Tamil Nadu High High | 165.7
Tamil Nadu High Low | 175.7
Tamil Nadu Low High | 176.93
Tamil Nadu Low Low | 183.2
Rajasthan High - | 108.62
Rajasthan Low - | 142.08
Chart: Procurement Cost – Per Annum
| Annual Procurement Cost (Crores)
Tamil Nadu High High | 72462.4
Tamil Nadu High Low | 76118.3
Tamil Nadu Low High | 77857.7
Tamil Nadu Low Low | 79060.2
Rajasthan High - | 57957.88
Rajasthan Low - | 70407.56

## Slide 21
FUTURE SCOPE
21
TAMIL NADU
(HIGH WIND)
UTTAR PRADESH
( HIGH MARKET PROCUREMENT)
NEW DELHI
(HIGH DEMAND WITH VERY LOW RES)
RAJASTHAN
(HIGH SOLAR)
POWER PROCUREMENT OF STATE DISCOMS
COMPARATIVE ANALYSIS OF STATE DISCOMS UNDER VARYING QUANTUM OF RE INTEGRATION
RES AVAILABILITY
RISK TAKEN BY DISCOM
Average
High
Low
No
Low
High
INTERNATIONAL CONFERENCE - COMMUNICATED
B. Ganesh, R. Vijay, P. Mathuria, R. Bhakar, “Short Term Power Procurement with Market Uncertainties for RE rich Indian Discom” communicated in IEEE Power and Energy Society – General Meeting, 2022.
PUBLICATIONS
FULL SCALE TOOL: API Software  GUI development

## Slide 22
REFERENCES
22
TYPE | S.No. | TITLE OF DOCUMENT | AGENCY | YEAR
REPORTS | 1 | 19th Electric Power Survey of India | EPS Committee | 2017
 | 2 | Pathways for TN’s Power sector 2020-2030 | NREL | 2020
 | 3 | Long Term Electricity Demand Forecasting | CEA | 2019
 | 4 | Daily Grid details | TANTRANSCO | 2021
 | 5 | India Energy Policy Review 2020 | IEA | 2020
 | 6 | Overview of Power Sector | PRS | 2019
 | 7 | Turning around the power distribution sector – Learnings & Practices from reforms | NITI Aayog | 2021
 | 8 | Monthly Report on Short Term transactions of electricity in India | CERC | 2021
 | 9 | DSM & related Regulations | CERC | 2021
 | 10 | Renewables Integration in India | NITI Aayog & IEA | 2021
 | 11 | Report of technical committee on study of optimal location various types of ESS to facilitate integration of RES and associated issues | CEA | 2017
 | 12 | Rethinking DISCOM Resource Planning in RE rich environment | USAID - MNRE | 2019
 | 13 | Power for All – Tamil Nadu | Govt. of India & TN | 2016
 | 14 | Determination of tariff for Generation & Distribution – Tamil Nadu | TNERC | 2017
 | 15 | Load Forecasting and Power Procurement Planning for Uttar Pradesh | IIT Kanpur | 2019

## Slide 23
REFERENCES
23
TYPE | S.No. | TITLE OF DOCUMENT | AGENCY | YEAR
WEBSITES | 16 | INDIAN ENERGY EXCHANGE https://www.iexindia.com/ | IEX, SEBI | 2021
 | 17 | MERIT ORDER DISPATCH https://www.meritindia.in/ | MoP, Govt. of India | 
 | 18 | CENTRAL ELECTRICITY REGULATORY COMMISSION https://cercind.gov.in/ | CERC | -
 | 19 | MINISTRY OF POWER https://powermin.gov.in/ | MoP, Govt. of India | 
 | 20 | RENEWABLES.NINJA https://www.renewables.ninja/ | Renewable Ninja | 
 | 21 | SOUTHERN REGIONAL LOAD DESPATCH CENTRE https://srldc.in/ | POSOCO | 
 | 22 | MINISTRY OF NEW AND RENEWABLE ENERGY https://mnre.gov.in/ | MNRE, Govt. of India | 
 | 23 | WESTERN REGIONAL LOAD DESPATCH CENTRE https://wrldc.in/ | POSOCO | 
 | 24 | ENERGY ANALYTICS LAB https://eal.iitk.ac.in/ | IIT Kanpur | 
PAPERS | 25 | Long Term electricity procurement portfolio optimization | EPSR, Elsevier | 2021
 | 26 | Discussion Paper on designing market for tertiary ancillary services in India | CERC | 2018
 | 27 | Risk Constrained Short Term Electricity Procurement for OA Consumer in India | NPSR, IEEE | 2016

## Slide 24
REFERENCES
24
[1] “India 2020 – Energy policy review,” IEA., Paris., France., Tech. Rep., Jan. 2020
[2] “Renewables integration in India,” NITI Aayog., New Delhi., India., IEA., Paris., France., Tech. Rep., Apr. 2021
[3] “Monthly report on short-term transactions of electricity in India,” Economics Division CERC., New Delhi., India.,
Tech. Rep., Mar. 2021
[4] P. Regy, R. Sarwal, C. Stranger, G. Fitzgerald, J. Ningthoujam, A. Gupta, N. Singh., “Turning around the power
distribution sector - learnings and best practices from reforms,” NITI Aayog., New Delhi., India., RMI India., New Delhi.,
India., Tech. Rep., Aug. 2021
[5] “Report of the technical committee on study of optimal location of various types of balancing energy sources/energy
storage devices to facilitate grid integration of renewable energy sources and associated issues,” CEA., New Delhi., India.,
Tech. Rep., Dec. 2017
[6] Central Electricity Regulatory Commission., accessed: 02 Nov. 2021 < https://cercind.gov.in/>
[7] C.K Simoglou, P.N Biskas, I.G Marneris, C.G Roumkos, “ Long-term electricity procurement portfolio optimization, ”
Electric Power Systems Research, vol. 202, Jan. 2021
[8] “19th Electric power survey of India, ” CEA., New Delhi., India., Tech. Rep., 2017
[9] Ministry of Power., <https://powermin.gov.in/>
[10] MERIT Order Dispatch of Electricity for Rejuvenation of Income and Transparency., <https://meritindia.in/>
[11] “Long term electricity demand forecasting, ” CEA., New Delhi., India., Tech. Rep., 2019
[12] “Rethinking DISCOM resource planning in renewable energy rich environment, ” USAID., USA., MNRE., India., 2019

## Slide 25
REFERENCES
25
[13] “Discussion paper on designing market for tertiary ancillary services in India, ” CERC., New Delhi., 2018
[14] A. Rose, I. Chernyakhovskiy, D. Palchak, M. Schwarz, S. Koebrich, M. Joshi., “Pathways for Tamil Nadu's electric power
sector: 2020 – 2030, ” NREL., Tech. Rep. Jan. 2021
[15] “Daily state load dispatch centre report, ” TANTRANSCO., Chennai, India
[16] “Determination of tariff for generation and distribution, ” TNERC., Chennai, India., Order in T.P. No.1of 2017
[17] “Power for All – TN document, ” A joint venture of Govt. of India and Govt. of TN., 2016
[18] A. Singh., “Load forecasting & power procurement planning for UP, ” IIT Kanpur., India
[19] P. Sharma, U. Brighu, R. Bhakar, P. Mathuria., “ Risk Constrained Short Term Electricity Procurement for Open Access
Consumer in India, ” IEEE., 2016
[20] P. Mishra, “Overview of the power sector,” PRS., Sept. 2019
[21] Indian Energy Exchange., accessed: 02 Nov. 2021 <https://www.iexindia.com/>
[22] Renewables.Ninja., accessed: 02 Nov. 2021 <https://www.renewables.ninja/>
[23] Southern Regional Load Despatch Centre., accessed: 02 Nov. 2021 <https://srldc.in/>
[24] Ministry of New and Renewable Energy., accessed: 02 Nov. 2021 <https://mnre.gov.in/>
[25] Western Regional Load Despatch Centre., accessed: 02 Nov. 2021 <https://wrldc.in/>
[26] Energy Analytics Lab., accessed: 02 Nov. 2021 < https://eal.iitk.ac.in/>